## Slide 1
CS447 Recitation #9: 4/2/18
Agenda for today:
Overview of Lab #10
  These slides are available online:
  https://github.com/kc13/CS447TK

## Slide 2
Lab #10 overview: Building a miniature MIPS processor
MiniMIPS Specifications:
Two registers (8 bits)
Only ALU and “set” instructions
  All instructions have a destination register
  All use the same instruction format

## Slide 3
MiniMIPS instruction set
$r = 0 if rd = A; $r = 1 if rd = B
MiniMIPS instruction format
- 16 bits long
- Addresses for instructions are 8 bits long

## Slide 4
Steps #1-2: Create the instruction memory
ROM component
A = Instruction address input (use default 8 bit width)
  Note hex format
D = Data output (16 bit instructions; be sure to adjust to 16).
  Note hex format, two values per row in display
  Right click to edit values
“sel”: wire a constant of ‘1’ to this

## Slide 5
Step #3: